# INTERSECTION/ CHANNELIZATION PLAN FOR APPROVAL CHECKLIST

# GENERAL REQUIREMENTS

Use latest version of Manual on Uniform Traffic Control Devices (MUTCD) and WSDOT Design Manual

# Plan scale 1”=30’ or 1” = 50’. Submit 22” x 34” plan sheets.

Have deviations/EUs been approved, if applicable (List any deviations/EU-s on plan sheets)

Submit a full size mylar copy for final approval (after review)

# DESIGN DATA BOX

State Functional Class (Principal Arterial, Minor Arterial or Collector)

City/County Functional Classification for crossroads

Access Control—Limited (Partial or Full) or Managed Class (1-5)

ADT

Percent Trucks

Design Vehicle(s)

Posted Speed and Design Speed

Distance (ft) to nearest intersections up station and down station of subject intersection (outside City limits only)

# TRAFFIC SCHEMATIC DRAWING

Current and Design year ADT

DHV for turning movements for current and design year

# PLAN SHEET

Project Title, State Route number, SR Milepost in title block

# Township, Range, Section, North Arrow, scale bar, legend, county

Street and Highway names

Right of Way lines (main line and crossroad)

Limited Access Control and turnback lines if applicable

Construction centerline, bearing, stationing or milepost

Begin/end stations and mileposts of roadway widening

Station, or milepost, and equations at centerline intersection of intersecting roads and approaches

# Angle of intersection

Curve data for each curve (curve radius, curve and tangent lengths, delta angle, PC, PI, PT and superelevation)

Vertical alignment - required if alignments are new or revised or if existing highway is in a vertical curve or

highway grades are greater than 5%.

Widths of lanes, turn lanes, shoulders, medians, curb & gutter, bike lanes, sidewalks, and bus pullouts

if applicable

Begin/end stations of channelization storage

Taper rates for lane transitions

Right turn corner radius and taper for intersecting roadways and approaches (DM Exhibit 1310-11)

# Intersection left turn radius

# Location and type of channelization (median curb, barrier, etc.)

Details for raised islands showing square footage, type of curb, etc.

# Block for approval signature and date

Block for stamping, signing and dating by registered professional engineer

ADDITIONAL INFO (To Be Included On Separate Sheets)

Intersection sight distance triangles (DM Exhibit 1310-22)

Auto Turn (Include design vehicle and turning radius)

Scaled raised island details w/ ADA dims, slopes, placement of signal and ped. poles